## Slide 1: Benchmarking SHA-2/ SHA-3 on MicroBlaze
By: Michael Rosales, Michael Yen, Nathaniel Case, and Noah Mendoza

## Slide 2: What This Presentation Discusses
Purpose: Benchmark SHA-2 and SHA-3 on MicroBlaze in constrained environments.
Why MicroBlaze? Customizable, ideal for embedded systems.
Metrics: Execution time, throughput, energy.
Insights: Efficiency vs. security trade-offs.
Impact: Informs secure algorithm selection.

## Slide 3: Motivations
Relevance: SHA-2/SHA-3 ensure secure communication and data integrity.
Need: Comparison driven by new cryptographic threats.
Focus: Constrained systems like IoT and CubeSats.
MicroBlaze: Customizable and ideal for benchmarking.
Impact: Balances efficiency and security insights.

## Slide 4: State of the Art Technology Relating to This
SHA-2: Efficient and widely used for secure communication, including digital signatures.
SHA-3: Enhanced security with sponge construction, resistant to physical attacks.
Bitcoin: SHA-256 is the primary hashing algorithm for mining and transactions.
IoT and Cloud Systems: SHA-3 is used in IoT devices, while SHA-2 and SHA-3 are integrated into cloud providers (AWS, Google Cloud, Azure).
MicroBlaze: Benchmarks provide insights into performance in constrained environments.

## Slide 5: System and Setup
Hardware: Nexys A7-100T FPGA with MicroBlaze processor.
01
Processor Configuration:
02
32-bit architecture, clocked at 100 MHz.
Instruction and data caches enabled.
DDR2 SDRAM added for larger datasets.
Peripherals:
03
AXI UARTLite for input/output.
AXI Timer for measuring cycles.
GPIO for debugging.
Software:
04
Open-source SHA-2 and SHA-3 implementations.
Xilinx Vitis for development and benchmarking.

## Slide 7: Performance Analytics
Test Cases: Functional tests, edge cases, and performance tests (1 KB and 1 MB inputs).
Metrics Analyzed:
Execution time (clock cycles).
Throughput (bytes per second).
Energy consumption (microjoules).
Tools Used: AXI Timer for execution time and calculated energy based on system power.
Key Inputs: Validated with the string "1234567890" and other edge cases.

## Slide 8: SHA 2-256 Vs. SHA 3-256
Execution Time: SHA 2-256 is faster; SHA 3-256 is slower due to sponge construction.
Throughput: SHA 2-256 achieves 12,288 bytes/s (1 KB), SHA 3-256 only 8,677 bytes/s.
Energy: SHA 2-256 is more efficient; SHA 3-256 uses more energy for larger inputs.
Conclusion: SHA 2-256 is better for efficiency, SHA 3-256 for stronger security.
 | SHA 3-256 |  |  | 
Test Type | Elapsed Cycles | Execution Time (µs) | Throughput (bytes/s) | Energy Consumed (µJ)
Edge Test (Empty Input) | 8436960 | 84369 | 0 | 16536
Performance Test (1KB) | 11801316 | 118013 | 8677 | 23130
Performance Test (1MB) | 509016809 | 5090168 | 118 | 997672
Functional Test (1234567890) | 8436959 | 84369 | 118 | 16536
 | SHA 2-256 |  |  | 
Test Type | Elapsed Cycles | Execution Time (µs) | Throughput (bytes/s) | Energy Consumed (µJ)
Edge Test (Empty Input) | 8332655 | 83326 | 0 | 92575
Performance Test (1KB) | 8332791 | 83327 | 12288 | 92576
Performance Test (1MB) | 550589815 | 5505898 | 109 | 6117052
Functional Test (1234567890) | 8332615 | 83326 | 120 | 92575

## Slide 9: SHA 2-384 Vs. SHA 3-384
Execution Time: SHA 2-384 is faster; SHA 3-384 slower for larger inputs.
Throughput: SHA 2-384: 8,777 bytes/s (1 KB), SHA 3-384: 6,245 bytes/s.
Energy: SHA 2-384 is more efficient; SHA 3-384 uses more energy.
Conclusion: SHA 2-384 excels in efficiency, SHA 3-384 in security.
 | SHA 2-384 |  |  | 
Test Type | Elapsed Cycles | Execution Time (µs) | Throughput (bytes/s) | Energy Consumed (µJ)
Edge Test (Empty Input) | 11665804 | 116658 | 0 | 116658
Performance Test (1KB) | 11665920 | 116659 | 8777 | 129608
Performance Test (1MB) | 686904071 | 6869040 | 87 | 7631503
Functional Test (1234567890) | 11665743 | 116657 | 85 | 129605
 | SHA 3-384 |  |  | 
Test Type | Elapsed Cycles | Execution Time (µs) | Throughput (bytes/s) | Energy Consumed (µJ)
Edge Test (Empty Input) | 11770011 | 117700 | 0 | 23069
Performance Test (1KB) | 16394718 | 163947 | 6245 | 32133
Performance Test (1MB) | 1966725523 | 19667255 | 30 | 3854781
Functional Test (1234567890) | 11770032 | 117700 | 84 | 23069

## Slide 10: SHA 2-512 Vs. SHA 3-512
Execution Time: SHA 2-512 is faster; SHA 3-512 is slower.
Throughput: SHA 2-512: 6,827 bytes/s; SHA 3-512: 4,489 bytes/s.
Energy: SHA 2-512 uses less energy; SHA 3-512 uses more for large inputs.
Conclusion: SHA 2-512 excels in efficiency; SHA 3-512 offers stronger security.
 | SHA 2-512 |  |  | 
Test Type | Elapsed Cycles | Execution Time (µs) | Throughput (bytes/s) | Energy Consumed (µJ)
Edge Test (Empty Input) | 14998762 | 149987 | 0 | 166635
Performance Test (1KB) | 14998927 | 149989 | 6827 | 166637
Performance Test (1MB) | 690268252 | 6902682 | 87 | 7668879
Functional Test (1234567890) | 14998773 | 149987 | 66 | 166635
 | SHA 3-512 |  |  | 
Test Type | Elapsed Cycles | Execution Time (µs) | Throughput (bytes/s) | Energy Consumed (µJ)
Edge Test (Empty Input) | 15103082 | 151030 | 0 | 29601
Performance Test (1KB) | 22810932 | 228109 | 4489 | 44709
Performance Test (1MB) | 422571709 | 4225717 | 142 | 828240
Functional Test (1234567890) | 15103077 | 151030 | 66 | 29601

## Slide 11: Edge Test and Functional Test

## Slide 12: Performance Tests (1MB/1KB)

## Slide 13: Conclusion
Hash Length: SHA-2 and SHA-3 outputs:
256-bit: 64 chars, 384-bit: 96 chars, 512-bit: 128 chars.
Performance: SHA-2 is faster; SHA-3 offers stronger security.
Energy: SHA-2 is efficient for small inputs; SHA-3 for larger ones.
Trade-offs: SHA-2 suits constrained systems; SHA-3 fits high-security needs.

## Slide 14: Future Works
Processor Comparison: Test algorithms on other processors, such as Intel Nios II or RISC-V.
Input Variability: Use larger, randomized, or real-world datasets (e.g., logs, sensor data).
Compiler Optimizations: Analyze performance using optimization flags like -O3.
Hardware Acceleration: Implement and compare hardware-accelerated versions on FPGA logic.
Power Profiling: Use precise tools to refine energy consumption analysis.